## Slide 1: OS Circulation environment “Trusted HTTP-FUSE Xenoppix”
http://unit.aist.go.jp/itri/knoppix/http-fuse/index-en.html
http://unit.aist.go.jp/itri/knoppix/xen/index-en.html
Kuniyasu Suzaki(1),Toshiki Yagi(1), Kengo Iijima(1),
Junichi Tsukamoto(2), Megumi Nakamura(3), Seiji Munetoh (3)
National Institute of Advanced Industrial Science and Technology
University of Tokyo
IBM Japan

## Slide 2: Contents
What is OS Circular?
  Virtual Bootloader “Xenoppix”
  Globalized Virtual Disk “HTTP-FUSE CLOOP”
Current Status
Conclusions
Demo

## Slide 3: Purpose of OS Circular
OS Migration System for anonymous Users
  Boot OSes on anonymous PC without installation.
FLOZ (Free Live OS Zoo) has same concept.
  http://www.oszoo.org/wiki/index.php/Free_Live_OS_Zoo
  “QEMU” runs OSes(Linux, Minix, Plan9, OpenSolaris, etc) on the server. The GUI is transferred by VNC on Client PC.
  Server Centric System
    Bad response because the server exits in Italy
    Guest OS has no network service for security & resource

## Slide 4: OS Circular
OS Circular is Client Centric System and utilize virtualization technology.
  Virtual Bootloader + Globalized Virtual Disks
  Client PC boots with the Virtual Bootloader and get OS images via Globalized Virtual Disks
    Current PC has powerful CPU, much Memory, and wide Network.
      It prevents server bottleneck. The network is managed by the user.
    OS images are maintained on the server and they are execute on a Client PC.
  Same idea is implemented on Collective[NSDI’05] and Internet Suspend/Resume[WMCSA’02]
    What is different?
    OS Circular utilizes existing, in-expensive and popular Infrastructure.

## Slide 5: Virtual BootLoader
Virtual Bootloader is consisted of “Virtual Machine software” and host OS which runs Virtual Machine
Virtual Machine offers an Abstraction Layer which offers a common PC environment on any PCes.
  Full Virtualization enables us to use normal installer and security management for Guest OS.
  The abstraction is used for OS migration.
    SoulPAD [Mobisys’05], VAT of Collective[NSDI’05], Internet Suspend/Resume[WMCSA’02 ] use VMware.
Host OS supports real device drivers
    KNOPPIX is used on SoulPAD and VAT of Collective, because KNOPPIX automatically detects available devices and loads the appropriate Linux drivers.

## Slide 6: Xenoppix as Virtual Bootloader
Xenoppix (2005.09～) = Xen + KNOPPIX
    Old Xenoppix uses Para-Virtualizaiton and runs Plan9 & NetBSD. Current Xenoppix runs Para & Ful Virtualizaion
  Full Virtualzation of Xen “HVM” prepares a common PC environment on anonymous PC.
    HVM requires virtualization instructions; Intel VT or AMD-V.
  KNOPPIX works on Domain0 of Xen (as the host OS).
    Xen has no device drivers and utilize the drivers of the OS on Domain0.“Autoconfig” of KNOPPIX detects devices and setup drives.
    So, Xen and KNOPPIX is the best marriage.

## Slide 7: Globalized Virtual Disk
Virtual Disk is Block Level Abstraction.
The requirement for globalization.
  Versioning
    Partial update
  Globalization
    World Wilde Deployment
    Network/Storage Transparent for mobile computing
      Handle network (dis/re)-connection
  Security
    OS itself should maintained by Security Software
    Virtual disks have to keep validness of contents

## Slide 8: Versioning
2 type of versioning
  Non-persistent versioning
    “undo” of operations during OS lives.
  persistent versioning
    “rollback” of OS image
Trusted HTTP-FUSE CLOOP has same versioning of Venti[USENIX’02] of Plan9.
  A SHA-1 hash of the data acts as the address of the data.
  Data blocks are write once and aren’t removed. They make ideal for permanent or backup storage.
  Unfortunately Venti requires special protocol for file system and limits the scalability.
Trusted HTTP-FUSE CLOOP saves data blocks to files.
  The feature makes to utilize HTTP to distribute them.

## Slide 9: Globalization (1/2)
Virtual disk are desired to be shared on Internet.
We must consider network latency and extensibility of server.
  NBD, iSCSI and iFCP look fine, but they require special software on server. This feature prevents scalability.
Policy of Trusted HTTP-FUSE CLOOP
  Don’t require special daemons and special ports on servers. The requirement is file distribution only.
  For World Wilde Deployment , utilize existing infrastructure.
    Web hosting services, Mirror servers, Proxies

## Slide 10: Globalization (2/2)
We have to consider dis-connection of network for mobile computing.
  StatelessLinux of RHEL5 takes snapshot on a local storage as cache.
The blocks of Trusted HTTP-FUSE CLOOP are cached on a local storage.
  While applications don’t access extra blocks, it works fine.

## Slide 11: Security
Basically security management is independent of virtual disk, because security of OS should be managed by security software or package manager.
The commitment of virtual disk is to keep uncontaminated contents.
Trusted HTTP-FUSE CLOOP check the validness of contents when it mapped to a virtual disk.

## Slide 12: HTTP-FUSE CLOOP (1/2)
Original block device is split by 256KB and compressed by zlib. Each data is saved to a block file.
Block files are managed by “index” file which works as a header of CLOOP.
Block file name is a SHA1 value of its contents.
  If there is a same contests blocks, they are held together a same name file and reduce total file space.
  The basic idea is resemble to “Venti of Plan9”
Block files are reconstructed to a CLOOP file by FUSE wrapper.
  FUSE is a User-land File System.
    http://fuse.sf.net
Each block file is measured with the SHA1 file name when it mapped to CLOOP.

## Slide 13: HTTP-FUSE CLOOP (2/2)
When a file is updated or created on an original block device, the relevant block files are newly created with new SHA1 name. The “index” file are also renewed.
  Old block files are reusable.
HTTP for file deliver
  Most popular and well designed.
    Web hosting is inexpensive.
    80 port is usually opened.
      Other network block devices use special port which is usually closed.
Block files are network/storage transparent.
  Block files are cached and reused on local storage.
  If necessary block files are stored in a local storage, network connection is not necessary.

## Slide 14
Block Device
256KB
…
4KB Page
ext2
…
…
…
index and block files
…
index.idx
4ad36ffe8…
974daf34a…
2d34ff3e1…
3310012a…
…
The block files are re-constructed as a virtual disk with HTTP-FUSE CLOOP
compressed
by zlib

## Slide 15
…
Contents SEVER
block files
…
Each block fie is measured with its file name
at reading
CLOOP file(700MB)
/cdrom/KNOPPIX
Loopback(2GB)
# losetup /dev/CLOOP
/cdrom/KNOPPIX
CLOOP
driver
cache 64KB
…
4KB Page
ext2
Access
decompress
extract
FUSE
driver
block files
/tmp/blocks
index.idx
header
(location data)
4ad36ffe8…
974daf34a…
2d34ff3e1…
3310012a…
…
Obtain in security

## Slide 17
Block Files
Cache files at
local storage
Full Virtualized VM
Index Files
HTTP Server
Client PC
Client PC
Internet
On demand
download
Security
Update
Master PC
New Block Files
New Index file
Updated OS

## Slide 18: Weak point of HTTP-FUSE CLOOP
HTTP-FUSE CLOOP is Vulnerable for Network Latency
  On demand & small data request makes narrow bandwidth on long latency.
Solutions
  Shorten Latency
    Find the nearest one among candidates dowonload sites
  Widen Bandwidth
    Pre download necessary block files
    Software RAID

## Slide 19: Care for network latency (Find near download site)
  Client Side Solution: netselect
    netselect measures the latency of candidate servers and finds nearest one.
      http://www.worldvisions.ca/~apenwarr/netselect/
  Server Side Solution: DNS-Balance
    DNS-Balance is a name resolver which suggests near candidate servers with routing information offered by RADB.net
      http://openlab.jp/dns_balance/dns_balance.html

## Slide 20: DNS-Balcance
DNS request
Resolve select.inetboot.net to shorten latency
XXX.168.0.10
YYY.10.0.19
Client
Web server for HTTP-FUSE Xenoppix
DNS server: ns.inetboot.net
Block files
resolve(DNS-banance)
select.inetboot.net
RADB
(Routing ASSET DATABASE)
ASK the nearest server for select.inetboot.net
XXX.168.0.10
YYY.10.0.19

## Slide 21: Care for network latency (Multiple download connections)
DLAHEAD (DownLoad AHEAD)
  Preparation
    Take a profile of downloaded block files at boot time.
  At boot time
    The block files are downloaded in advance with extra download connections. (Default is 4)
  Effective and easy to implement
Software RAID using MD
  Mirroring(RAID1) virtual block device makes fault tolerant and broadband with multiple access.

## Slide 22: Current Status of OS Circular
Virtual Boot Loader
  Xenoppix (Xen 3.0.3 + KNOPPIX 5.0.1)
  Debian package
    HTTP-FUSE CLOOP
    Setup script for OS Circular
OS Images is obtained by Trusted HTTP-FUSE CLOOP
  Debian GNU/Linux
    Secure updated with “apt-get” command
  FreeBSD

## Slide 23: Current HTTP sites
Web Hosting Service is reasonable.
  5GB/ mount from $10

## Slide 24: Discussions
Live OS update
  Intel vPro, LUCOS[VEE’06]
  We have plan to integrate IDS and IPS on OS Circular.
BlkTap of Xen [USENIX’05]
  Xen offers an interface of software device “BlkTap”.
  We want to make an offload engine of Trusted HTTP-FUSE CLOOP.

## Slide 25: Conclusions
OS Circular is Client Centric OS Migration System which is consisted of Virtual Bootloader “Xenoppix” and Global Virtual Disk “Trusted HTTP-FUSE CLOOP”.
The current target OSes are Debian GNU/Linux and FreeBSD.
  Debian is updated by “apt-get” automatically.
We hope OS Circular easy-to-try OS environment.

## Slide 26
Loopback setup
VFS
CLOOP
ext3
/vdisk/vdisk0
/tmp/blocks/＊＊＊
glibc
libfuse
fuse-wrapper
libcurl
FUSE
Userspace
Kernel
Internet
Reconstract CLOOP file from block files.
File
System
Block Device
libcrypto
Measure each block file
“Index file”
Obtain in security
/dev/cloop0
Xen HVM
disk=[‘phy:/dev/cloop0,hda1,ro’ ]

## Slide 27
CLOOP file
Block Device
(2GB)
64KB
…
4KB Page
ext2
…
…
…
block files named by MD5
64KB
…
4KB Page
ext2
…
…
…
Update
apt-get install …
…
index.idx
4ad36ffe8…
974daf34a…
2d34ff3e1…
3310012a…
…
FUSE
driver
Same files
Reusable for FUSE
…
index.idx
4ad36ffe8…
dd4daf34a…
2d34ff3e1…
3310012a…
…
CLOOP style
block file style