Suspend to Disk
Why it doesn't work, can't work and never worked in the first place
(and what to do about it)
Matthew Garrett
<mjg59@srcf.ucam.org>

---
This presentation contains no drosophila

---
What is suspend to disk?
Save system state to disk
Reboot directly into saved state
Consumes no power when suspended
Higher latency in resume

---
How does suspend to disk work?
Freeze processes
Suspend devices
Copy state
Restore devices
Save state to disk
Power down
Cake

---
The cake is a lie

---
Freezer nightmare

---
What else can go wrong?
Your swap is on a FUSE filesystem
You have userspace USB drivers
Your network driver blocks while scanning
NFS
  - (Without loss of generality)

---
Why do we use the freezer?
Because we're suspending using the same kernel as we were running

---
How can we avoid this?
Use a different kernel?

---
Kexec
Functionality for loading a new kernel and executing it
  - Kexecing a new kernel is an atomic operation
New kernel can save state to disk without interfering with the “real” kernel
  - Has its own i/o paths, working with its own RAM
Ying Huang at Intel working on this

---
Still stuck with the freezer...
Drivers assume that userspace will be frozen
  - (Silly drivers)
But those need to be fixed anyway, so hurrah

---
Warning: next slide contains crack

---
Do we really want to suspend to disk?
Users just want to retain state
Checkpointing applications handles a lot of this
Saving hardware state more awkward
  - But buys us more functionality

---
Summary:
The freezer is unreliable and cannot sensibly be made reliable
Suspend to disk must be a reliable process
Therefore we need to remove the need for the freezer
(Cake)

---
Please hire me
I'm lovely, really